United Nations Population Fund, UNFPA

International Zone (IZ) – UNAMI compound – D2 building

Iraq

Website: iraq.unfpa.org/

Date: 08 October 2016

Request for Quotation No. UNFPA/IRQ/RFQ/16/015

Dear Sir/Madam,

We hereby solicit your quotation for the supply of Medical supplies as Specified in Annex1 of this RFQ.

If you are interested in submitting a quotation for these items, kindly fill in the attached Quotation Submission Form – Annex 2, and send by email to: bid.iraq@unfpa.org or the address indicated below not later than 16 October 2016, and 17:00 (GMT+3).

Name of Contact Person in UNFPA: 	Mr. Habeeb Abdulla

Street address:	Iraq – Baghdad – International Zone (IZ) – UNAMI compound – D2 building – UNFPA office

Tel No.: 009647719963311

Email: bid.iraq@unfpa.org

Quotations submitted by email must be free from any form of virus or corrupted contents, or the quotations shall be rejected.

It shall remain your responsibility to ensure that your quotation will reach the address above on or before the deadline. Quotations that are received by UNFPA after the deadline indicated above, for whatever reason, shall not be considered for evaluation.  If you are submitting your quotation by email, kindly ensure that it is signed and in the .pdf format, and free from any virus or corrupted files.

Full acceptance of the UNFPA General Terms and Conditions is mandatory. They can be located on this webpage at: http://www.unfpa.org/resources/unfpa-general-conditions-contract . Non-acceptance of the terms of the General Terms and Conditions (GTC) shall be grounds for disqualification from this procurement process.

Note: Current UNFPA supplier policies apply to this solicitation and can be found at: http://www.unfpa.org/suppliers.

Please take note of the following requirements and conditions pertaining to the supply of the abovementioned goods:

| Goods | All the goods to be supplied under the contract may have their origin in any country should be international standard |
| --- | --- |
| Delivery Terms [INCOTERMS 2010] | CPT/CFR (Erbil, Iraq) |
| Customs clearance, if needed, shall be done by: | UNFPA Country Office Iraq |
| Insurance | Cargo Insurance is covered by UNFPA global insurance policy. Please do not include insurance costs in your quotation. |
| Delivery Location | Erbil, Iraq |
| Delivery Schedule | Required |
| Mode of Transport | LAND |
| Currency of Quotation | United States Dollars |
| Documents to be submitted | Duly Accomplished Form as provided in Annex 2, and in accordance with the list of requirements in Annex 1; A statement whether any import or export licenses are required in respect of the goods to be purchased including any restrictions on the country of origin, use/dual use nature of goods or services, including and disposition to end users; Confirmation that licenses of this nature have been obtained in the past and an expectation of obtaining all the necessary licenses should the quotation be selected; Your previous experience of supplying UN agencies (which agency, when, where, what kind of product) Your company profile, date of establishment, number of staff, legal registration, current licenses List of other clients Catalogs, including images for all items specified in Annex 1 Manufacturing dates for medical supplies From where you got information about our RFQ Your company address, and telephone and name of contact person Quality Certificates (ISO, etc.); Certificate of Exclusive Distributorship in the country (if applicable, and if Supplier is not the manufacturer); Written Self-Declaration of not being included in the UN Security Council 1267/1989 list, UN Procurement Division List or other UN Ineligibility List; |
| Period of Validity of Quotes starting the Submission Date | 60 days |
| Delivery time | 07 to 15 days upon issuing PO |
| Partial Quotes | Permitted |
| Partial Delivery | Permitted |
| Payment Terms | 100% after delivery |
| Evaluation Criteria | Full compliance to requirements and lowest price Full acceptance of the UNFPA General Terms and Conditions |
| UNFPA will award to: | One or more suppliers |
| Type of Contract to be Signed | Purchase Order |
| Conditions for Release of Payment | Written Acceptance of Goods of beneficiary based on full compliance with RFQ requirements |
| Annexes to this RFQ | Specifications of the Goods Required (Annex 1) Quotation Form (Annex 2) Annex 2 need to be duly completed and submitted in order to qualify for the procurement process. |
| Special Condition | Offers without documents specified will not be considered Vendors should strictly follow delivery time |

Annex 1

Technical Specifications

| Items to be Supplied | Quantity | Specifications of Goods |
| --- | --- | --- |
| Wheel chair | 08 | Weight capacity 140 kgs - Manual |
| O2 cylinders with regulators | 10 | Standard Flow Rate: 40 l/min Maximum Flow Rate: 150 l/min Single Stage Pressure Regulator with Flowmeter 0-15 l/per min. Pre-Set Pressure Relief Valve, calibrated at 10 bar Vertical/Horizontal Positioning available 6cm long adaptor between flowmeter & regulator Tubing Nipple Every unit rigorously tested prior to dispatch Batch Number stamped on regulator for identification purposes Comply fully with the requirements of HTM 2022 |
| Sonic aid | 12 | Heart Rate Display (LCD) Automatic Display Freezing After remove from the body Heart Rate Range 50-240 bpm Accuracy ± 2 or 2% Ultrasound Frequency 2MHz Ultrasound Intensity <10mW/cm2 Out put Headset with Volume Control Double Audio Output sockets for Headset Power Supply: 1.5V Battery x 2 Sensitivity From 10 - 12 weeks PC Interface cable |
| Gynecological Bed | 12 | All sections fit with padded mattresses, entirely detachable from bed for easy cleaning Mattress covers removable via side zipper Transfer bars connect all lower distal portions of the 4 supports, providing maximal structural strength Body section: Mounted on 4 sturdy supports, all finished with height adjustable feet Padded knee crutches are height and width adjustable, set with robust clamps with heavy knob Fixing of the crutch holders is solid steel and welded to the frame of the bed Leg section: Mounted on 4 swivel castors, heavy duty, all 4 with brakes This section can be lowered and recesses entirely under the body section When fully extended, both the body and leg section align to perfectly flat surface Body section, including mattress: 120 x 80 x 80 cm (l x w x h) Leg section, including mattress: 70 x 75 x 80 cm (l x w x h) Frame: 3 cm (outside, across), 2 mm (thickness) Swivel castor wheel: 3 x 10 cm (w x diameter) Mattresses: 10 cm (h) Carrying capacity: 150 kg |
| Patient's beds, two movements | 30 |  |
| Portable light source (celling light) chargeable | 10 | A light used during examinations or treatment of the patient. It is usually used during examination or treatment during minor events Designed to be easily moved from one location to another. Arm: 105 +/- cm articulated, spring loaded arm, arm with on/off switch and incorporated electronically transformer. Integral rechargeable battery for operation without mains electricity. Mobile stand with swivel castors. Lamp emits natural white light: colour temperature approx. 4000 K. Halogen bulb approx. 12V/20W Light intensity: approx 20.000 Lux at 40 cm. Reflector adjustable for positioning. Free cord: length approx 3 m. Power supply: The supplier has to supply the right voltage, plug and socket type that fit the country it is delivering the goods to. The country of destination would be stated in the UNFPA’s PO. Supplied with: 1 x spare bulb a 1x spare fuse. 1x Instructions for use: Manual with instructions for use, cleaning, diagrams for assembly/disassembly (if applicable) and maintenance , storage and handling in English, French, and Spanish) Accessories/ spare parts/consumables 1 spare fuse 1 spare bulb |
| Infant Weighing Scale | 10 | Max. 12 Kgs Digital scale |
| Portable ultrasound | 08 | Portable high-performance ultrasound system, main unit. Full digital portable model Compact and lightweight, easy to carry via handle Size Size WDH, 31.5* 35.3* 25.3cm, Weight 6.4kg Monitor with screen: easy operation handling Scanning method: electronic convex sector probe, electronic linear, also support endo-rectal probes Imaging display modes: , B, B+B, B+M, B+M/M, M, 4B Imaging technologies: dynamic frequency imaging, multi-stage focusing and aperture control. Image gray-scale: 256 levels Depth range selection: convex sector image and linear image, 16 steps adjustable Image orientation: support for lateral and vertical inversion (in B mode). 128-frame CINE loop . 90-frame image storage |
| Suction machine 1.5 - 2 Liters capacity, electric, with infant and adult tubes | 10(1,000 adult tubes and 1,000 infant tube) | For use in minor surgical procedures, E.N.T., resuscitation and for aspiration of secretions, pus, bloods etc. Mounted on a stable, portable stand with castors/wheels and handle Castors / wheels to have fully 360 degree swivel, minimum size 75mm. Sturdy shock resistant casing, easy to carry and easy clean. Vacuum Extractor for intermittent and continuous suction. Reciprocating, oil free pump, twin piston type (metallic). Adjustable suction from 0-675mm/Hg (800 mbar) Suction flow maximum, approximately 17L/minute Capable of being stored continuously in ambient temperature of 0 to 50 deg C and relative humidity of 15 to 100%. Capable of operating continuously in ambient temperature of 10 to 40 deg C and relative humidity of 15 to 100%. Suction pipe length: approx. 1.5 m. Explosion proof foot switch for control of vacuum (vacuum 9 bar) Supplied with graduated plastic jar auto-clavable of 3 litters with overflow safety device and antibacterial filter Power supply: The supplier has to supply the right voltage, plug and socket type that fit the country it is delivering the goods to. The country of destination would be stated in the UNFPA’s PO. Power consumption, approximately 100W Material: Graduated jar: polysulphone Connection/suction tube: silicone (medical grade Supplied with: Sterilizable/disposable silicone tubes set for molar aspiration & missed abortion sizes 6, 7, 8, 9 and 10 mm , length approximately 2.5m Connectors for fitting the silicone tubes. Instruction for user: manual with instructions for assembly, use and maintenance, and list accessories and spare parts, in 3 languages (English, French and Spanish). Accessories/Spare parts/Consumables: 1 x Set of silicone tubes 1 x Set of connectors fitting the silicone tubes 1 x Spare jar with cover, gasket and overflow valve 1 x Set of spare antibacterial filters 1 x Set of spare fuses |
| Infant Radiant Warmer | 05 | 1, Skin temp, and manual control by micro-computer 2, Over temperature alarm 3, Available adjustment of radiator and mattress tilting 4, With one illumination light 5, APGAR timer |
| Mobile examination light | 25 | A light used during examinations or treatment of the patient. It is usually used during examination or treatment during minor events Designed to be easily moved from one location to another. Arm: 105 +/- cm articulated, spring loaded arm, arm with on/off switch and incorporated electronically transformer. Integral rechargeable battery for operation without mains electricity. Mobile stand with swivel castors. Lamp emits natural white light: colour temperature approx. 4000 K. |
| Instrument table | 60 | Metal Instrument table with wheels |
| IV stands | 60 | Metal |
| HB Meter | 15 |  |
| Autoclave 24 liters | 10 | Steam sterilizer, pressure type, capacity 24 litres. Product Description: Steam sterilizer/autoclave for sterilizing medical materials such as dressings and surgical instruments under superheated steam. Metal vessel with high-pressure seal suitable for sterilization under superheated steam. Maximum pressure: 21 PSI / 1.5 bar. Maximum temperature: 259ºF / 126ºC. Metal to metal seal (no rubber gaskets). Safety clamping locks: retaining bayonet clamp and (6) Bakelite wing nuts to prevent displacement of cover while sterilizer is under pressure. Inner Chamber dimensions: Chamber, approximately: diameter 315mm x height 290mm. Aluminium container, approximately: diameter 285mm x height 250mm. Sterilization capacity, approximately: 24 litres. Removable cover equipped with: Bakelite handle. Dial type geared steam gauge graduated in kg / cm², PSI and degrees Fahrenheit, and with colour-coding showing sterilizing zone (green) and caution zone (red). Control valve and flexible metal exhaust tube. Excess pressure relief valve and over-pressure rubber plug. Supplied with: 1 x spare over pressure rubber plug Instructions for use and cleaning/maintenance and with diagrams for assembly/disassembly; in 3 languages (English, French and Spanish). Listing of parts, accessories and spare parts. |
| Incubator | 04 | 1. Servo Control Mode: Air temperature, skin temperature; 2. Instant Parameter Displaying: Set temp, air temp, skin temp, internal humidity, heat power rate 3. Audible & Visual Alarms: Power failure, sensor failure, higher & lower temp, air& skin temp override, fan failure, system failure; 4. >37° C Preset Mode: Power failure reset memory, alarm silence, keypad lock, self-test function; 5. Hood with dual slope: 6 hand-ports; Left & right cabinets, top-shelf; Display parameters: - Patient temperature - Air Temperature - Visual and audible alarms for: i. Patient and air high/low temperature alarm. ii. Air circulation / probe / system / power failure alarm. iii. Humidity alarm. - Temporal alarm silencer. - Heater power indicator |
| Sphygmomanometer | 25 | Type: Blood Pressure Monitor Measure:0-300mmHg, Aluminium, Manual |
| Stethoscope | 25 | Dual Head Stethoscope, dual head chestpiece with non-chill rubber rings, binaural, aluminium with plastic tips. Supplied with spare diaphragm and two pair soft eartips. |
| Lab Water Bath | 04 | Laboratory water bath with cover (lid), 15 liter inner tank, stainless steel with following features: Stabilizing temperature at 25, 37, 42 or 56°C. Temperature of bath must be maintained within a narrow range +0.1°C. Microprocessor PID-control, timer digital display, overtemperature Cut-out. |
| Centrifuge | 04 | Centrifuge, tabletop Electronic control panel max. speed 6,000 rpm, with RCF of 3461 Timer 1-99 min./continuous/short cycle mode (impulse key) with revolution indicator. With 8x15ml angle rotor for tubes 17x100 mm. Accessories: Adapter no. 1054, PP, 8/set @ EUR 92.5 for glass tubes 5 ml (12x75 mm) or vacutainer 13x75 mm with Hemogard cap or Greiner Vacuette 13x75 mm with cap |
| Micro Centrifuge | 04 | Micro centrifuge, tabletop, high-speed, up to 15,000 rpm with following specifications: Bench top microcentrifuge, with speed range 500-15000rpm, timer 0-99minuts + hold, 10 progamme memory, 10 acceleration rates and 10 deceleration rates. With fixed angle rotor 24-place for 1.5/2ml microtubes (tube size max 11x50mm) |
| Spectrophotometer | 04 | Spectrophotometer, UV/Visible range 190-1000nm for basic applications Microprocessor – controlled UV/VIS spectrophotometer shall have single beam operation with automatic reference corrected measurements The unit shall feature a holographic grating monochromator with a range from 190-1000mm Optical Banwidth: 4nm LCD display Keyboard controlled Modes - Absorbance, % Transmission of sample, Standard curve method, Coefficient method Wavelength accuracy shall approximately be with 1nm Program selectable photometer range should measure within a –0.3 to 3.0A operating range Auto lamp and filter selection The spectrophotometer shall perform a self test and calibration. Power requirements 220VAC, 50/60Hz |
| Laboratory light microscope | 04 | Laboratory light Microscope, binocular type, with standard set. Microscope with frame-Binocular tube-Pair of eyepiece 10X (FN20) -Quadruple revolving nosepiece -Mechanical stage (right handle) -Abbe condenser -AS-Blue filter -30W illuminator-6V30W halogen bulb -Plan objectives 4X, 10X, 40X -Power cord -Dust cover No. 015 |
| Thermometer | 30 | Thermometer, ear, electronic, Thermometer, digital in °C with large display - display range 25°C - 42°C, Memory: last reading, beeper function, auto shut-off, provided in plastic case. |
| Cusco's Speculum Large size | 30 |  |
| Cusco's Speculum Medium size | 15 |  |
| Laryngoscope | 15 |  |
| Anesthetic Machine | 02 | Stable sturdy construction on 4 antistatic swivel castors, 2 with brakes. Trolley with upper shelf that to mount a monitor in a flexible and easy way, allowing an ergonomic viewing Handles facilitate positioning of the machine. Movable arm holder for supporting patient breathing circuit. If O2 / N2O supplied by bottle, holders for bottles to include secure locking mechanism. Material tubing and mask: DEHP free Externally supplied anaesthetic gas, oxygen and air mixture ratios fully controllable. Separate flow control for O2, N20 and anaesthetic agents. Rotameter tubes 0 to 10L/minute for O2 and N2O Mixer secures a minimum of 25% oxygen Gas supply gauges required, with scales allowing easy reading.Gas supply input 2 to 6bar Minimum of 2 vaporizers. Nebuliser to deliver particle size of < 3 micron and to be used in both offline and online modes. Soda lime absorber, with 2.5kg reservoir and adjustable pressure limiting valve Non-return and three way valve, with connecting tube Ventilator: Modes Automatic Volumetric (IPPV) and Manual Pneumatically driven, electronically controlled compressor, minute volume 2 to 25L/minute Tidal volume 20 to 1500ml Respiratory rate 5 to 70 cycles/minute I/E ratio 2/1 to 1/4 Inspiration pressure 0 to 80mbar Peak inspiratory flow 0 to 60L/minute Trigger sensitivity 0 to -20mbar Display fit with broncho manometer, range approximately -10 to 100mbar Facility to measure and display on screen: a) 3 traces against time: pressure, volume and flow b) 3 two-axis displays: Pressure-Volume, Flow-Volume and Pressure-Flow c) Airway pressure (Peak and Mean). d) Tidal volume (Inspired and Expired). e) Minute volume (Inspired and Expired). f) I:E ratio g) inspiration and expiration times h) Spontaneous Minute Volume i) Respiratory rate (spontaneous and mechanical). j) Total Frequency. k) Oxygen concentration l) End tidal CO2 with capnography m) FiO2 dynamic. n) Intrinsic PEEP and PEEPi Volume. o) Plateau Pressure. p) Resistance and Compliance. Trend display facility for at least the last 8 hours, with minimum 5 minutes resolution Automatic compliance and leakage compensation for circuit and tubes. Front panel shows status, errors and sensors failure (low/high pressure, power failure) Audio-visual alert on low/high pressure, apnoea, power failure Display of operational status, with set and measured values Front panel shows status and errors (low/high pressure, power failure, battery status) Safety features for hypoxic mixtures, oxygen failure (emergency O2 bypass), overpressures Self-diagnosis with each start-up and integrity testing of all system parameters With adjustable patient-circuit support arm Built-in rechargeable battery, autonomy approximately 2 hours Automatic switch to battery in case of power failure, automatic recharge when connected to mains Power supply: The supplier has to supply the right voltage, plug and socket type that fit the country it is delivering the goods to. The country of destination would be stated in the UNFPA’s PO. Power input to be fitted with compatible mains plug. Voltage corrector / stabilizer to allow operation at ± 30% of local rated voltage. Resettable overcurrent breaker required on both live and neutral supply lines. Voltage corrector / stabilizer to allow operation at ± 30% of local rated voltage. An internal battery capable of powering the unit for at least 30 minutes. Supplied with: 1 x Paediatric reusable breathing circuit (tubes/balloons/valves/masks) 1 x Adult reusable breathing circuits (tubes/balloons/valves/masks) 2 x Soda lime absorber grains, pack/2.5kg 1 x Spare parts/maintenance kit (air filters, tubing, O-rings) 2 x Sets of reusable masks, each of: small, medium and large (textured for easy fit) 1 x Set of spare fuses 1 x Instructions for assembly, use and maintenance, and list of accessories and spare parts with product reference code, in 3 languages (English, French and Spanish) Accessories/ spare parts/consumables 1 x Paediatric reusable breathing circuit (tubes/balloons/valves/masks) 1 x Adult reusable breathing circuits (tubes/balloons/valves/masks) 2 x Soda lime absorber grains, pack/2.5kg 1 x Spare parts/maintenance kit (air filters, tubing, O-rings) 2 x Sets of reusable masks,, each of: small, medium and large (textured for easy fit) 1 x Set of spare fuses 1 x Instructions for assembly, use and maintenance, and list of accessories and spare parts with product reference code, in 3 languages (English, French and Spanish) |
| Operating Table | 02 | General purpose operating table, 4 areas, 5 sections Stainless steel finished base on 4 castors Central brake lowers the table onto 4 robust, height adjustable feet Solid reinforced base creates maximum stability, with patient, up to the limits of each position Base is fit with earth connection Gear, lever and crank mechanisms are all manually operated, no gas springs Radiolucent table top with integrated standard size x-ray cassette channels All sections fit with a mattress, detachable for easy cleaning Mattresses have welded seams, core and surface are joined Table adjustable to all essential positions Height adjustable with foot-pedal via hydraulic lever system Factory filled with hydraulic oil Three areas adjustable via manual crank: back, pelvic and legs Backrest adjustable 0 to +60 degree Trendelenburg and reverse Trendelenburg: +/- 25 degree Lateral tilting, both sides: +/- 20 degree Leg area removable, consists of 2 independent sections, each adjustable to a combination of up/down and left/right Head area removable, and independently adjustable, +20 to -90 degree Accessories on both sides clamp on standard stainless steel medical rail When elevated and fully extended, all sections align to perfectly flat surface Materials: High resistance to corrosion (tropical environment) Frame: Austenitic stainless steel 18/10 Table top: radiolucent epoxy resin Sliders/fixtures rail for accessories: Austenitic stainless steel 18/10 Mattress: welded seams rubber, highly tear resistant, anti-static, flame retardant, disinfectant- and liquid proof, washable Caster frame/bracket: steel Caster wheel: single wheel, solid, non-hooded (for easy maintenance) Dimensions: Operating table, all areas extended: 210 x 50 x 70 to 100 cm (l x w x h) Height adjustment: 70 to 100 cm (h) Height adjustable feet, footprint: 6 cm (diameter) Mattress: 5 cm (h) Carrying capacity: 150kg Construction: Knockdown construction: no Supplied with: 1 x complete set of tools required for assembly 4 x spare fixation clamps 1 x set fitting mattresses 1 x spray bottle of silicon (for mattress maintenance) Set of accessories, each with fixation clamp: 1 x anaesthesia screen arc 2 x lateral support, height adjustable only 2 x shoulder support, height and width adjustable 2 x leg support 2 x arm board, with arm fixation strap, vertical and horizontal adjustable 2 x padded knee support, lithotomy crutch, with fixation strap 1 x body strap |

Annex 2

Quotation Form

Name of Bidder:

Date of Bid:

Request for Quotation No:

Currency of Bid price:

Delivery time (7 to 15 days upon issuing PO):

Expiration of Validity of Quotation (The quotation shall be

valid for a period of at least 60 days after the Closing date.):

Price Schedule:

| Item No. | FOB/FCA price/unit specify port of shipment | Quantity | Transportation cost to port of Destination (specify mode of trp.) | Total CPT/CFR (Destination port) | Delivery schedule (months) |
| --- | --- | --- | --- | --- | --- |

I hereby certify that this company, which I am duly authorized to sign for, accepts the terms and conditions of UNFPA and we will abide by this quotation until it expires.

Name and title					Date and Place

# Text boxes

Vendor’s Comments: